## Slide 1
3DGPU
3D Graphics Processing Unit
ECE 495D
Tuesday, 2:30-5:20pm
TA: Philip Vorsilak
Given 04/19/05
Final Presentation
James Doty
Kyle McGhee
Allan Patterson
Daniel Wilhelm

## Slide 2
Introduction
High-Level Organization
Block Specifics
Remaining Work/Conclusions
Outline
Introduction
3DGPU A 3D graphics processing unit designed for high-end cellular phones.

## Slide 3
User Features
Introduction
Hardware-accelerated rendering of points and lines
Hardware-accelerated depth-ordering of primitives
Automatic perspective projection for realistic feel
Intended for small LCD displays, 256x256, with 8-bit color
Operates synchronously with CPU

## Slide 4
Technical Features
Introduction
8-bit w-buffer
Page flipping architecture
Pass-by-value opcodes utilized for speed
Two separate SRAM modules
Variable frequency display output
Line algorithm optimized for hardware
Use 16:16 fixed point numbers
Modifiable field of view

## Slide 5
OPCODE | MNEMONIC | DESCRIPTION
0000 | setmat addr_MATRIX | Set Current Matrix.
0001 | mulmat addr_MATRIX | Multiply Current Matrix.
0010 | rstmat | Reset Current Matrix to Identity.
0011 | xfov val_FIXED | Set X Field of View.
0100 | yfov val_FIXED | Set Y Field of View.
0101 | pt3d addr_3DVEC | Draw 3D point.
0110 | ln3d addr_3DVEC addr_3DVEC | Draw 3D line.
0111 | color val_COLOR | Set Color.
1000 | clr | Clear Buffer.
1001 | flip | Page Flip.
1010 | pt2d addr_2DVEC | Draw 2D point.
1011 | ln2d addr_2DVEC addr_2DVEC | Draw 2D line.
1100 | XXX | UNUSED
1101 | XXX | UNUSED
1110 | XXX | UNUSED
1111 | XXX | UNUSED
Supported Opcodes
High-Level Organization

## Slide 6
Block Diagram
High-Level Organization

## Slide 7
Block Diagram
High-Level Organization

## Slide 8
Shift Register
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
SYNTHESIZED! Area: 0.128 mm²

## Slide 9
Controller
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register

## Slide 10
Controller
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
SYNTHESIZED! Area: 0.228 mm²

## Slide 11
Matrix Math
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register

## Slide 12
Matrix Math
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
SYNTHESIZED! Area: 13.8 mm²

## Slide 13
3D Projection
Input: (2.5, 2.5, 1.0); (200.0, 125.25, 11.5) xFOV = 1.0, yFOV = 0.866
Output: (2, 3, 1); (17, 12, 11)
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
UNSYNTHESIZED, NEEDED DIVIDER

## Slide 14
Line Rasterization
Input: (7, 5, 0)->(10, 15, 16)
Output: (7, 5, 0); (8, 8, 5); (9, 12, 11); (10, 15, 16)
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
UNSYNTHESIZED, NEEDED DIVIDER

## Slide 15
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
Divider
SYNTHESIZED! Area: 0.429 mm²

## Slide 16
Screen Buffer
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register

## Slide 17
Screen Buffer
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
SYNTHESIZED! Area: 0.0155 mm²

## Slide 18
SRAM Controller
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
SYNTHESIZED! Area: 0.00730 mm²

## Slide 19
LCD Controller
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
SYNTHESIZED! Area: 0.00586 mm²

## Slide 20
LCD Simulator
Controller
Matrix Math
3D Projection
Line
Rasterization
Screen Buffer
SRAM
Controller
LCD
Controller
LCD Sim
(C Code)
Divider
Shift
Register
C# CODE

## Slide 21
Future Work
Conclusions
Implement division module with 3D Projector and Line Rasterization
Integration of individual modules
Develop animated 3D testbenches for playback
Prepare timing and area analyses
Lessons Learned
More top-level GPU/CPU research before programming
Determine target clock rates in advance

## Slide 22
Questions
Conclusions
Questions?